## Slide 1: Authentication via Visible Light Communication
Dan Whitcomb

## Slide 2: Visible Light Communication

## Slide 3: Modern day
LEDs:
Up to 500 Mb/s
Multichannel
Photodiodes

## Slide 5: Mobile: Screen to Camera
Parallel Communications
Serial Communications
Notes: ----- Meeting Notes (11/18/14 12:24) -----
None of these options offer serial communication with devices that only one person has

## Slide 6: What does everyone have?

## Slide 7: Mobile LED to Camera

## Slide 8: Security Analysis
Advantages
Common device pairings
Small/localized transfer space
Others don’t know time of transfer (theoretically)
Disadvantages
Few unified transfer standards – not every application works together
Frame synchronization

## Slide 9: Method
iOS:
1. Converts ASCII string to binary
2. Flashes at time interval

## Slide 10: Method
Mac OSX
OpenCV – computer vision library – does frame processing
Average brightness of ‘1’
Grayscale
Threshold
Avg Brightness – Standard Deviation
Repeat
Threshold to Zero Operation
OpenCV
Notes: ----- Meeting Notes (11/18/14 12:24) -----

## Slide 11: Testing
20 rounds per variable
9 bits – ASCII ‘w’ + 1 start bit – per test (001110111)
Varying bit analysis thresholds (std dev multipliers)
Varying bit rates
Results
Slow bit rate => Higher success rate
Bit accuracy not variable
Max 60% success rate per 8 bits @ 1 second

## Slide 12: Analysis
Poor performance with larger keys
- 2bit/sec => 0.02%
success rate for 128 bit key
- 10bit/sec => 6.5536 ×
10^-10% success rate @
128bit key
Transfer rate limited by camera’s frame rate => can be decoded by looking
iSight camera ambient light sensor; auto adjustments
Changing to bits of different values is less accurate
‘w’ = 0 0 1 1 1 0 1 1 1

## Slide 13: Verdict
My implementation not suitable for security needs
Useful in theory => photodiode in computer is necessary.